## Slide 1: CMPE 207 Network Programming and Applications

## Slide 2: Audio/Video Streaming Services
Typically sensitive to delay, but can tolerate packet loss
Data contains audio and video content (“continuous media”)
Example applications
  Streaming stored media: RealAudio/RealVideo
  Unidirectional real-time: online course broadcast
  Interactive real-time: video conference
Notes: Streaming stored audio/video:
- Clients request audio/video files from servers and pipeline reception
over the network and display
- Interactive: User can control operation (similar to VCR: pause, resume,
fast forward, rewind, etc)
- Delay: from client request until display start can be 1 to 10 seconds
- Example: RealAudio/RealVideo
Streaming live audio/video (Unidirectional):
- Similar to existing TV and radio stations, but delivery on the network
- Non-interactive, just listen/view
- Example: online course broadcast
Streaming live audio/video (Interactive)
- Phone conversation or video conference
- More stringent delay requirement than Streaming and Unidirectional
because of interactive real-time nature

## Slide 3: Internet Audio/Video Applications

## Slide 4: Real Time Delivery (Audio/Video)
Packet network nature
  Delay, unpredictable delay
  Loss
Consequences  countermeasure
  Pkts arrive out of order  reordering
  Pkts arrive out of sync  jitter buffer
  Pkts lost  acknowledgement and retransmission
    Real time delivery: No retransmission
Mechanism
  Order – sequence number – used in packet handling
    +1 each packet  gaps = loss
  Time – encoding timestamp – used in playback
    Encoding time, arrival time and playback time
    Can also be used for delay & jitter calculation

## Slide 5: Interactive Audio/Video
Sending Side
  A sequence number on each packet is required
  An encoding timestamp is required on each packet
  Even if there is no packets transmitted (e.g. silence), encoding timestamp is always ticking
  Same timestamp may appear on multiple packets
Receiving Side
  A playback buffer is required for jitter processing
  In general, packet receiving time is different from packet playback time (delayed playback)
  Packet playback time is based on the “encoding timestamp”
  If packet is not available during playback, concealment methods are used to fill the gap (packet loss recovery)
  Real-time traffic needs the support of multicasting
  Translation means changing the encoding of a payload to a lower quality to match the bandwidth of the receiving network
  Mixing means combining several streams of traffic into one stream (conferencing)

## Slide 6: Audio/Video Transport Protocols
TCP, with all its sophistication, is not suitable
UDP is more suitable
  However, we need the services of RTP, another transport layer protocol, to make up for the deficiencies of UDP.
RTP (Real-time Transport Protocol)
  Data transfer protocol to handle real-time traffic
  RTP does not have a delivery mechanism; it must be used with UDP.
RTCP (RTP Control Protocol)
  A companion protocol of RTP for control information communication

## Slide 7
RTCP
RFC 1889
(RTP, RTCP) pair

## Slide 8: RTP Packet Header
granularity determined by payload type
# contributor
ver 2
if this RTP stream is mixed

## Slide 9: Timestamp, SSRC, CSRC
Timestamp – encoding time
  Clock granularity determined by payload type
  Initial timestamp is a random number chosen by the sending application
  Support silence suppression
    If no packets are sent during periods of silence, the next RTP packet may have a timestamp significantly greater than the previous RTP packet.
Synchronization Source (SSRC)
  32-bit identifier
  The entity setting the sequence number and timestamp
    Normally the sender of the RTP packet
  Chosen randomly, independent of the network address
    Meant to be globally unique within a session
  May be a sender or a mixer
Contributing Source (CSRC)
  Used to identify the original sources of media behind the mixer
  0-15 CSRC entries

## Slide 10: RTCP (RTP Control Protocol)
A companion control protocol of RTP
Separate data (RTP) and control (RTCP)
RTCP allows endpoints to periodically exchange control information
  For quality-related feedback and other meta-information
A third party can also monitor session quality and detect network problems
  Using RTCP and IP multicast
RTP port
  Typically even-numbered UDP port, not fixed port
  RTCP port = RTP port (even) + 1
  Default RTP/RTCP uses UDP port 5004/5005
Typical UDP size limited to few hundred bytes
Typical: one media (audio, video, …) per port pair
RTCP is optional

## Slide 11: RTCP Types
Sender Report (SR): 200
  Time info for each SSRC and bytes sent
  Timestamp  synchronization among multiple RTP streams (e.g. audio/video)
Reception Reports (RR): 201
  Report number of packets received and expected  loss, jitter, round-trip delay
Source Description (SDES): 202
  Description of user who owns source
  Separate from SSRC which might change
Explicit Leave (BYE): 203
  Who leaves session, in addition to time-out
Extensions (APP): application-specific
VER | P | RC | PTYPE | LENGTH
Data Area … |  |  |  | 

## Slide 12: RTSP (Real Time Streaming Protocol)
RTSP establishes and controls either a single or several time-synchronized streams of continuous media such as audio and video
  Interactive control
    Play, stop, pause, fast-fwd, rewind, etc (aka network remote control)
  Media retrieval
    The client can request a presentation description and ask the server to set up a session to send the requested media data
  Adding media to an existing session
    The server or the client can notify each other about any additional media becoming available to the established session.
Provides means for choosing delivery channels
  UDP, multicast UDP, or TCP
  Default RTSP control channel port number: 554
RTSP is similar to HTTP/1.1 in terms of syntax and operation, but
  RTSP is stateful
  RTSP works in both directions, both client and server can initiate requests

## Slide 13: RTP and RTSP
RTSP provides users VCR-style control
  RTSP allows two-way communication; that is, viewers can communicate with the streaming server and do things like rewind the movie, go to a chapter, and so on
    E.g. QuickTime automatically translates the viewer interaction with the on-screen movie controller into the proper RTSP requests
  By contrast, RTP is a one-way protocol used to send live or stored streams from the server to the client.
RTSP doesn’t include transmission of streaming data itself
  RTSP servers often use RTP/RTCP for media stream delivery

## Slide 14: RTSP Directives
DESCRIBE | Retrieves the description of a presentation
ANNOUNCE | Change the description (can go either direction)
GET_PARAMETER | Retrieves the value of a parameter
OPTIONS | Queries the available methods
PAUSE | Streams delivery is halted temporarily
PLAY | Starts sending data
RECORD | Starts receiving data
REDIRECT | Informs to connection another server location
SETUP | Specifies the transport mechanism
SET_PARAMETER | Requests to set the value of a parameter
TEARDOWN | Stops the stream delivery and frees the resources

## Slide 15: RTSP Usage Example
Client queries request types Server accepts
    Client  Server:
    OPTIONS rtsp://192.168.1.1:8554/demo.mp3 RTSP/1.0
    CSeq: 2
    Client  Server:
    RTSP/1.0 200 OK
    Content-Length: 0
    Cseq: 2
    Public: DESCRIBE,SETUP,TEARDOWN,PLAY,PAUSE,GET_PARAMETER

## Slide 16: RTSP Usage Example
Client retrieves the description of a presentation
    DESCRIBE rtsp://192.168.1.1:8554/demo.mp3 RTSP/1.0
    CSeq: 3
    Accept: application/sdp
    RTSP/1.0 200 OK
    Content-type: application/sdp
    Content-Base: rtsp://192.168.1.1:8554/demo.mp3
    Content-length: 343
    Cseq: 3
    v=0
    …
    a=control:rtsp://127.0.0.1:8554/demo.mp3
    m=audio 0 RTP/AVP 14
    b=AS:128
    b=RR:0
    a=rtpmap:14 MPA/90000/2
    a=control:rtsp://192.168.1.1:8554/demo.mp3/trackID=2

## Slide 17: RTSP Usage Example
Client specifies RTP as the transport mechanism
    SETUP rtsp://192.168.1.1:8554/demo.mp3/trackID=2 RTSP/1.0
    CSeq: 4
    Transport: RTP/AVP;unicast;client_port=59030-59031
    RTSP/1.0 200 OK
    Transport: RTP/AVP/UDP:unicast;client_port=59030-59031;server_port=53481-53482;ssrc=8E199999;mode=play
    Session: 609e2146c2f29e5d;timeout=60
    Content-length: 0
    Cseq: 4

## Slide 18: RTSP Usage Example
Client requests to play the stream
    PLAY rtsp://192.168.1.1:8554/demo.mp3 RTSP/1.0
    CSeq: 5
    Session: 609e2146c2f29e5d
    Range: npt=0.000-
    RTSP/1.0 200 OK
    RTP-Info: url=rtsp://192.168.1.1:8554/demo.mp3/trackID=2;seq=55364;rtptime=1893179874
    Range: npt=781.257806-
    Session: 609e2146c2f29e5d;timeout=60
    Content-length: 0
    Cseq: 5

## Slide 19: RTSP Usage Example
After a while, Client terminates the stream session
    TEARDOWN rtsp://192.168.1.1:8554/demo.mp3 RTSP/1.0
    CSeq: 9
    Session: 609e2146c2f29e5d
    RTSP/1.0 200 OK
    Session: 609e2146c2f29e5d;timeout=60
    Content-length:0
    Cseq: 9